## Slide 1: Cascode Current Mirror
FILS – Integrated Circuits

## Slide 2
Simple Current Mirror - Reminder
When a simple current mirror is used, there is an error introduced by the channel length modulation effect. The output current is not exactly equal to the input current as the two transistors do not work at the same Vds voltage.
The simple current mirror (small signal equivalent) output resistance is limited by the output transistor output resistance, ro.

## Slide 3
Cascode Current Mirror
A solution to this problem is to decouple the MN1 drain from the output voltage variation.
This is achieved by the MN2 transistor.
So we have
We assume MN2 to be in saturation. This assumption will give us the output voltage allowed range. With this assumption:
This is a constant voltage. (We assumed the mirror to be 1:1 ratio. Otherwise there will be a (W/L)1/(W/L)3 scaling factor in front of Ib, but the voltage will still be constant.)
As Vb is also constant, this means Vds1 is constant.
This means that MN1 drain – source voltage was decoupled from VO.
MN1 is still influenced by channel length modulation, but has a constant Vds voltage and it’s current will also be constant.

## Slide 4
Cascode Current Mirror
Limitations
Of course, the compensation is not perfect. MN2 is also affected by channel length modulation. Taking this into account, MN2 saturation equation is:
So Vgs2 actually depends on the output voltage even if MN2 is in saturation. This means that Vds1=Vb-Vgs2 will also depend on VO.
Any variation of Vds1 will lead to a variation of the output current (through the channel length modulation effect).
So the effect is not completely removed, but it is greatly reduced.
Taking this into account, and the fact that Vds2=VO–Vds1, we have

## Slide 5
Cascode Current Mirror
Output voltage range (Ro: excursia tensiunii de iesire)
This analysis was done under the assumption that MN2 is in saturation. The condition for this is:
Replacing this, we get:
We would like to express this as a function of the output voltage.
We can express Vds2 as:
If MN2 is no longer in saturation (crosses to the linear region), MN2 will start acting as an open switch and the output voltage variation will be seen in MN1 drain. The MN1, MN3 mirror will still be functional until MN1 enters linear region, but it will work as a simple current mirror. All benefits from the cascode stage will (gradually) disappear.

## Slide 6
Cascode Current Mirror
Choosing Vb voltage.
From the previous slide, we have seen that, the smaller we choose Vb, the higher the output voltage range is.
However, there is a lower limit to Vb. For the MN1, MN3 mirror to function properly, MN1 transistor needs to be in saturation.
This means that the minimum Vb voltage is given by
On the other hand, MN1 and MN3 transistors should have the same drain – source voltage if we want them to have the same current.
For this schematic, Vds3=Vgs3=Vgs1. We can choose Vb such that Vds1 also equals Vgs1. Namely:
This is a good choice and it is widely used, but it does not provide the maximum output voltage range.
Another option is to change the schematic so that MN3 has a lower Vds voltage.

## Slide 7
Cascode Current Mirror

## Slide 8
Cascode Current Mirror – Small Signal Circuit
MOS transistor small signal equivalent circuit:
Cascode current mirror small signal equivalent circuit:

## Slide 9
Cascode Current Mirror – Small Signal Circuit
As for the simple current mirror, we are interested in the equivalent output resistance.
We are not applying any signal so there is no gain to calculate.
To do this, we will apply an external small signal VO voltage and we will determine RO=VO/IO.
First we solve for G3 node.
So (as before) we can simplify the schematic

## Slide 10
Cascode Current Mirror – Small Signal Circuit
Now we cab solve for IO.
But usually gm2ro1ro2>>ro1 or ro2, so we have:

## Slide 11
Cascode Current Mirror – Generating Vb potential
We shall now discuss several (3 to be precise) topologies to generate the Vb voltage.
First, let us review the conditions we have identified so far for the Vb voltage:
  Vb should be high enough so that MN1 is in saturation
  Vb should be chosen such that MN1 and MN3 have the same drain source voltage
To this, we will add the observation that the lower we choose Vb, the larger the output volage range will be.

## Slide 12
Cascode Current Mirror – Generating Vb potential
The first, simplest and most widely used topology just uses a diode connected transistor, MN4, to generate Vb.
We have:
So Vds1 is given by:
MN2 and MN4 should be designed to have the same Vgs voltage
This is easily achieved if MN2 and MN4 are identical transistors biased at the same current.
MN3 is diode connected, so Vds3=Vgs3. So we get:
We note that, as Vgs1=Vgs3 and Vgs2=Vgs4, Vb is also given by:

## Slide 13
Cascode Current Mirror – Generating Vb potential
The minimum output voltage is given by
In conclusion, this schematic keeps MN1 in saturation (Vds1=Vds3>Vov1) and keeps Vds1=Vds3.
However, Vb is significantly higher than Vb,min
This also means that the output voltage range is not optimized

## Slide 14
Cascode Current Mirror – Generating Vb potential
Intermediate schematic – Not to be used!
Having Vb defined by two Vgs voltages always leads reduced output voltage range.
One option is to use one Vgs voltage instead, as shown in the schematic below.
However, in this schematic Vds1 is no longer equal to Vds3.
This would introduce a systematic offset in the output current.

## Slide 15
Cascode Current Mirror – Generating Vb potential
In this schematic we have introduced MN5 transistor to control MN3 drain voltage.
First, let us concentrate on defining Vb voltage.
In this case, we have
So we get:
But, for MN1 to be in saturation, Vds1 needs to be larger or equal to Vov1. This gives the condition for Vov4.
Regarding Vds1=Vds3 condition, we have:
MN5 an MN2 can be sized to have equal Vgs voltage (identical transistors biased at same current), so we get:

## Slide 16
Cascode Current Mirror – Generating Vb potential
Sizing MN4
We will size MN4 (determine (W/L)4) in order to full have
All transistors are in saturation, we have
This gives us:
For simplicity, we assume (W/L)1=(W/L)2. We then have:

## Slide 17
Cascode Current Mirror – Generating Vb potential
An alternative way of generating the Vb voltage is presented in this schematic. We have
Assuming Vgs2=Vgs3, we get
This means we need to size the resistor R so that we get the desired Vds1 value (so that MN1 is in saturation).
We also have:
If we assume Vgs4=Vgs2, we also have: